## Slide 1: Notes on SVN tag tiegcm1.92_r296
New lower boundary coding scheme (module lbc.F)
New lower boundary option to use SABER/TIDI data
New namelist read parameter Kp (see flow diagram)
Increase night-time electron densities (qinite.F)
Bug fix in Weimer05 (wei05sc.F)
Change calculation of sun’s location from dipole to apex
Update IGRF coefficients with IGRF11 (apex_subs.F)
Use collective function mpi_bcast (mp_updatephi)
Script changes to enable MPI runs on HAO 64-bit systems
Several minor bug fixes

## Slide 2: tiegcm1.92_r296 is in $TGCMROOT
To make default serial run on HAO Linux machines:
  cp $TGCMROOT/tiegcm1.92_r296/scripts/tiegcm-linux.job .
  tiegcm-linux.job >&! tiegcm-linux.out &
To make default MPI run on 64-bit HAO Linux machines:
  cp $TGCMROOT/tiegcm1.92_r296/scripts/tiegcm-linux.job .
  In job script: set mpi=TRUE, and set nproc=4
  tiegcm-linux.job >&! tiegcm-linux.out & (type pw 3 times)
To make default run on IBM bluefire:
  cp $TGCMROOT/tiegcm1.92_r296/scripts/tiegcm-ibm.job .
  bsub < tiegcm-ibm.job
To checkout code from SVN repository:
  svn checkout $SVN/tiegcm/tags/tiegcm1.92_r296

## Slide 3
Potential Model
Heelis
Weimer05
IMF Data
User Specified
GPI Data
User Specified
Kp
Namelist Input:
Kp
Power= f(Kp)
Ctpoten=f(Kp)
bx,by,bz
swden,swvel
Namelist Input:
bx,by,bz
swden,swvel
Namelist Input: power,ctpoten
High-Latitude Input Options in tiegcm1.92_r296
Power= f(Kp)
Ctpoten=f(Kp)
Power=f(bz,swvel)
Ctpoten=f(Weimer phihm)
Power=f(bz,swvel)
Ctpoten=f(Weimer phihm)
Aurora
Aurora
Aurora
Default
This diagram shows input options specifying the potential model to be used for high-latitude ion convection, and options for input or calculation of cross-tail potential and hemispheric power, which drive the auroral parameterization. See notes on the following pages.

## Slide 4
Notes:
Potential models output high-latitude electric potential, which is used to calculate ion drift velocities.
IMF data is optionally used to drive the Weimer potential model.
GPI Kp data is optionally used to calculate ctpoten and power, which drive the auroral parameterization.
GPI f10.7 solar flux data is optionally used to calculate heating and ionization rates (not shown in diagram)
Notes and restrictions on namelist inputs:
Heelis and Weimer potential models are mutually exclusive.
If GPI or IMF data are requested, user can still override with namelist, but must NOT provide at least one parameter. Data will be used for parameter(s) not provided by the user.
If missing data is encountered in data files, the program will stop with an error message.
GPI data cannot be used in a Weimer run, and IMF data cannot be used in a Heelis run.
User cannot provide Kp in a Weimer run (data or no data)
If Kp is provided, at least one of ctpoten and power must NOT be provided.
Namelist Input Parameters (“User Specified” and “Namelist Input” in the diagram):
(Several of these are optional, see notes and restrictions)
(ctpoten, power, kp, bximf,byimf,bzimf, swvel, swden may be constants or time-dependent)
potential_model = [‘HEELIS’ or ‘WEIMER’]
imf_ncfile = [netcdf data file containing bx,by,bz,swden,swvel]
gpi_ncfile = [netcdf data file containing Kp, f10.7]
ctpoten = [cross-cap potential drop (Kv)]
power = [hemispheric power (GW)]
f10.7d = [Daily f10.7 cm flux]
f10.7a = [Average f10.7 cm flux]
kp = [Kp index]
bximf,byimf,bzimf = [components of IMF (on separate lines)
swvel, swden = [solar wind velocity and density (on separate lines)

## Slide 5
Functions:
Power=f(Kp):
Function hp_from_kp (util.F)
If (kp <= 7) hp = 16.82*exp(0.32*kp)-4.86
If (kp > 7) hp = 153.13+(kp-7)/(9-7)*(300-153.13)
Ctpoten=f(Kp)
Function ctpoten_from_kp (util.F)
ctpoten = 15+15*kp+0.8*kp**2
Power=f(bz,swvel):
Function hp_from_bz_swvel (util.F)
fac = 2.0
If (bz < 0) hp = 6+3.3*abs(bz)+(0.05+0.003*abs(bz))*(min(swvel,700)-300)
If (bz >= 0) hp = 5.0+0.05*(min(swvel,700)-300)
hp = max(2.5,hp)*fac
Ctpoten=f(Weimer phihm) (wei05sc.F):
weictpoten(ih) = 0.001*(vnx(ih,2)-vnx(ih,1))
ctpoten = 0.5*(weictpoten(1)+weictpoten(2))